## Slide 1
Adaptive predictive control for pipelined multiprocessor image-based control systems considering workload variations
Sajid Mohamed1, Nilay Saraf2, Daniele Bernardini3, Dip Goswami1, Twan Basten1, Alberto Bemporad2
1Eindhoven University of Technology, The Netherlands
2IMT School for Advanced Studies, Lucca, Italy
3ODYS S.r.l., Italy
This research has received partial funding from the EU’s H2020 FP under GA no 674875 (oCPS) and the ECSEL JU under GA no 783162 (FitOptiVis).

## Slide 2: Image-based control (IBC) system – an example
vehicle on road
desired lateral
deviation
lateral deviation
steering angle
disturbance
measure states
Control Strategies
Embedded Platform
Vision-based lateral control of a vehicle
Dynamic system (continuous time)
S : Sensing & processing
C : Control computation
Embedded Platform (discrete-time)
camera(s)
A : Actuation

## Slide 3: IBC system characteristics: workload variations
C
S
A
C
S
A
C
S
A
idle time
idle time
best-case
worst-case
workload distribution
Execution time of ‘S’ depends on image workload variations
Variable relatively long sensing delay
Do not know the exact sequence of occurrence of image workload apriori

## Slide 4: IBC system: typical design
C
S
A
C
S
A
time (ms)
0
100
C
S
A
idle time
60 fps
idle time
dropped frames
(
(
τ
best-case
worst-case
workload distribution
Controllers typically designed for worst-case workload  rarely happens
Dropped frames and unnecessary idle times
rarely happens

## Slide 5: IBC system: research question
C
S
A
C
S
A
C
S
A
idle time
idle time
best-case
worst-case
workload distribution
How to cope with this long, variable sensing delay to improve system performance?

## Slide 6: Multiprocessor IBC system
Multiprocessors are common and relatively cheap
Highly suitable for IBC system implementation
Pipelined implementation – focus of this work
  Reduces sampling period
  Maximal pipelined implementation: when h = fh
A
C
S
S
A
C
S
A
C
A
C
S
S
A
C
S
A
C
A
C
A
C
Core 1
Core 2
Core 3
...
camera input
τ
time

## Slide 7: Multiprocessor IBC system: practical challenges
Workload variations
Platform constraints
  E.g. number of available processing cores
System non-linearities
  E.g. velocity of the car is varying
Constraints on system variables
  E.g. maximum steering angle is constrained to +/- 25 degree
Inter-frame dependencies
*see paper for references of related work

## Slide 8: Inter-frame dependencies
Data or algorithmic dependencies – video coding, visual tracking
fd – time required to wait between processing consecutive image frames
dropped frames
A
C
S
S
A
C
A
C
S
S
A
C
Core 1
Core 2
Core 3
...
camera input
τ
Core 4
Cannot start the next frame processing as

## Slide 9: Multiprocessor IBC system: practical challenges
Workload variations
Platform constraints
  E.g. number of available processing cores
System non-linearities
  E.g. velocity of the car is varying
Constraints on system variables
  E.g. maximum steering angle is constrained to +/- 25 degree
Inter-frame dependencies
*see paper for references of related work
Not fully addressed for pipelining in state-of-the-art* multiprocessor IBC system implementations!

## Slide 10: Contributions
An adaptive predictive control formulation for a pipelined multiprocessor IBC system implementation
  based on linear parameter-varying (LPV) input/output (I/O) models of IBC systems
  Considering
    Workload variations
    Inter-frame dependencies
    System non-linearities
    Constraints
Tutorial overview of handling delay while using I/O models for MPC
How can we optimise Quality-of-Control for a practical real-life IBC system?

## Slide 11: Is it feasible to use MPC in resource-constrained systems?
Yes, due to recent advances in numerical optimization for MPC
  Implemented in automotive domain
    engine control* and power train coordination^
What about adaptive MPC?
  Model and MPC tuning parameters can be adapted at run time without reconstructing the optimization problem~
  Computational complexity is same as the non-adaptive case
  Fast enough for resource-constrained embedded applications
*A. Bemporad et al., “Model predictive control of turbocharged gasoline engines for mass production,” SAE Technical Paper, 2018.
^A. Bemporad et al., “Supervisory MPC of a powertrain with a continuously variable transmission,” SAE Technical Paper, 2018.
~N. Saraf and A. Bemporad, https://arxiv.org/pdf/1908.07247, 2019

## Slide 12: Considering inter-frame dependencies and platform constraints
Adaptation with inter-frame dependencies and camera frame arrival period fh
Adaptation with available number of processing cores and fh
#cores for maximal pipelined implementation
Notes: n_c^{max} :The number of processing cores needed to realise the maximal pipelined implementation

## Slide 13: MPC formulation
MPC Formulation
I/O system model
Platform constraints, fd  sampling period and delays
Adaptive predictive control system

## Slide 14: MPC formulation
Optimization problem formulation
Penalise output tracking error
Penalise deviation of inputs from steady-state targets
Stack of known past sequence of outputs and inputs
: Prediction horizon; determines the #decision variables
: Control horizon; determines the #decision variables
Notes: The input sequence that is optimized is typically restricted to fewer variables for trading-off control performance with computations via the control horizon (Nu) constraint.
Note that the future values of parameters p can be incorporated as they may be known and in that case p represents p(k+l) in the LPV model.

## Slide 15: Adaptive predictive control formulation
I/O model – can be derived from state-space model as well (see paper for details)
Incorporate workload variations as a variable delay in I/O model
  For .
The size of the MPC problem does not change
Tuning parameters and model parameters can all be changed at run-time

## Slide 16: Predictive control strategy
Adaptation with workload variations
sensing & processing
controller
actuation
case 3
case 2
case 1
A
C
A
C
A
C
A
C
A
C
A
C
A
C
A
C
...
...
Core 1
Core 2
Core 3
...

## Slide 17: Predictive control strategy
  Case 1: sensing delay is same as the previous step
    nd is kept constant, stack updated as usual
  Case 2: sensing delay is increased by one step
    Latest measurement is not available
    nd is incremented by 1, stack of past outputs is not updated
  Case 3: sensing delay is reduced by one or more steps
    Latest and past measurement(s) are available
    nd is reduced accordingly, stack updated iteratively with the available measurements
controller
actuation
case 3
case 2
case 1
Adaptation with workload variations

## Slide 18: Simulation results
For an efficient MPC implementation: QP problem transformed to box-constrained least-squared problem [N. Saraf and A. Bemporad, ArXiV 2019]
Control performance evaluation
  Inter-frame dependence time: fd = 15 ms
  System nonlinearity: vx is a ramp signal
  Constraints: |steering angle| = 0.5 radians
  Workload variations: PERT distribution
Notes: Specifically, the QP problem (5) is transformed to the following box-constrained
least-squares problem by eliminating equality constraints
through quadratic penalties with large weight

## Slide 19: Comparison with state-of-the-art
MPC is relatively compute-intensive
  Worst-case control computation time is 15x greater than LQR-based control
  Still only ~6 ms for our case, assuming ~50MHz processor.
Advantages as compared to other approaches
  Considers inter-frame dependencies
  Modelling and considering system nonlinearities
  Strictly imposing constraints on the system variables
See paper for detailed comparisons

## Slide 20: Conclusions and future work
A step towards real-life adoption of IBC system
Reduce the gap between current state-of-the-art multiprocessor IBC approaches and practical control requirements
Future work:
Real-life implementation
  Starting with IMACS SiL/HiL framework*
*www.es.ele.tue.nl/~dgoswami/imacs

## Slide 21
Adaptive predictive control for pipelined multiprocessor image-based control systems considering workload variations
Sajid Mohamed1, Nilay Saraf2, Daniele Bernardini3, Dip Goswami1, Twan Basten1, Alberto Bemporad2
1Eindhoven University of Technology, The Netherlands
2IMT School for Advanced Studies, Lucca, Italy
3ODYS S.r.l., Italy
This research has received partial funding from the EU’s H2020 FP under GA no 674875 (oCPS) and the ECSEL JU under GA no 783162 (FitOptiVis).
S.Mohamed@tue.nl linkedin.com/in/sajidmohamed